## Slide 1: Reducing DRAM Latency via Charge-Level-Aware Look-Ahead Partial Restoration
Yaohua Wang, Arash Tavakkol, Lois Orosa, Saugata Ghose,
Nika Mansouri Ghiasi, Minesh Patel, Jeremie S. Kim,
Hasan Hassan, Mohammad Sadrosadati, Onur Mutlu
October 22, 2018
Notes: I will present our work named reducing DRAM latency by Charge-level-aware look-ahead partial restoration.

## Slide 2: Executive Summary
DRAM access latency has not decreased significantly for decades
  A DRAM cell stores data as charge, where the charge leaks over time
  Requires row activation and charge restoration: high-latency operations
  We can reduce the latency by only partially restoring a cell’s charge level
Key observations
  There is significant potential to reduce latency if we partially restore DRAM cells that will be reactivated soon
  If we reduce restoration too much, we cannot use mechanisms that reduce the activation latency: need to strike a balance
CAL: Charge-Level-Aware Look-Ahead Partial Restoration
  Simple prediction for rows that will be reactivated soon (98% accuracy)
  Maximizes the total DRAM access latency reduction using both partial restoration and reduced activation latency
  8-core workloads: 14.7% speedup, 11.3% energy reduction on average
Notes: Let’s first take a high level overview of this work.
DRAM latency is a major bottleneck for system performance
[click]
DRAM cells store data as charge, where the charge leaks over time
[click]
Accessing DRAM cells requires row activation and charge restoration, which are two major components of DRAM latency
[click]
To reduce DRAM latency, we can just partially restoring a cell’s charge level.
[click]
We observe that the potential of partial restoration can be significantly increased when applied on cells that will be accessed again soon
[click]
We also find that we can trade-off between restoration and activation latency reductions to achieve the benefits of both
[click]
Based on our observations, we propose charge level aware look ahead partial restoration, we call it CAL
[click]
CAL predicts the next access-to-access interval
[click]
And then it Applies partial restoration based on the prediction and trade-off between restoration and activation latency reductions
[click]
Overall, CAL achieves 14.7% performance improvement and 11.3% of energy reduction for an 8-core system

## Slide 3: Background: Accessing Data in DRAM Key Observations on Partial Restoration Charge-Level-Aware Look-Ahead Partial Restoration Evaluation Conclusion
Outline
Notes: I will first provide necessary background on DRAM

## Slide 4: Fundamental DRAM Operations
Activation (ACT)
Restoration
DRAM Cell
Row Buffer
Refresh
Precharge (PRE)
R/W
PRE
tRCD
tRAS
MemCtrl
CPU
Timeline
ACT
Notes: Processors always incorporate a Memory Controller which handles the communication with the DRAM module.
[click]
A DRAM chip, which builds up the DRAM module, consists of DRAM cells and row buffer as shown in the right-side.
When accessing data in DRAM.
[click]
Activation opens one of the DRAM rows, and copies the data into the row buffer to serve reads or writes.
[click]
The time passed from Activation to the state when the row buffer is ready to serve READ or WRITE, is defined by tRCD
[click]
As DRAM cells’ charge is drained during activation.
Restoration restores the charge to maintain the data integrity.
[click]
The time taken from the start of the ACT to the completion of Restoration is called tRAS, only after restoration
[click]
precharge command can be issued,
[click]
which releases the data from the row buffer. This prepares DRAM to activate a different row.
[click]
As DRAM cells lose charge overtime.
[click]
To prevent data loss, DRAM cells are periodically refreshed.

## Slide 5: Reducing Latency with Partial Restoration
Prior work [Zhang+ HPCA ’16] exploits the charge level of a DRAM cell by partially restoring the cell’s charge
  Refreshes are regularly scheduled every 64ms
  Baseline: charge level is fully restored after refresh or access
  Apply partial restoration for soon-to-be refreshed cells
Full
Min
Charge Level
64ms
Ref
Ref
Full
Min
Charge Level
Acc
Acc
Ref
Ref
Decay
64ms
Acc
Acc
Full Charge Restoration
Partial Restoration
Notes: Prior work exploits the charge level of a DRAM cell by partially restoring the cell’s charge
[click]
As mentioned above, DRAM cells lose charge overtime,
refreshes are regularly scheduled every 64ms to fully restore cells’ charge level
[click]
Aside from refresh, each DRAM access also fully restores the charge level
[click]
The key idea of the prior work is that if the cell will be refreshed soon, Partial restoration can be applied to restore just enough charge and leave the refresh to fully restore the charge level. And thus, achieving reduced restoration latency.

## Slide 6: Background: Accessing Data in DRAM Key Observations on Partial Restoration Charge-Level-Aware Look-Ahead Partial Restoration Evaluation Conclusion
Outline
Notes: Now I will provide our own observations on partial restoration

## Slide 7: More Significant Opportunities for Partial Restoration
We can partially restore a cell if it will be reactivated soon
On average, 95% of access-to-access intervals are <16ms
Large potential benefits for partial restoration, but how can we predict when a cell will be reactivated?
Chart: Interval Distribution
| mix1 | mix2 | mix3 | mix4 | mix5 | mix6 | mix7 | mix8 | mix9 | mix10
[0,16] | 0.99599 | 0.98603 | 0.97308 | 0.98373 | 0.96795 | 0.9663 | 0.98645 | 0.98822 | 0.9784 | 0.96737
[16,32] | 0.00035287 | 0.0058132 | 0.0061899 | 0.0059188 | 0.0098412 | 0.014679 | 0.0022288 | 0.001427 | 0.0060145 | 0.010067
[32,48] | 0.00026599 | 0.00060912 | 0.0077618 | 0.0026858 | 0.0093318 | 0.0082669 | 0.0044968 | 0.0013425 | 0.0045584 | 0.0054467
[48,64] | 0.00047945 | 0.0004288 | 0.001878 | 0.0017247 | 0.0012603 | 0.00098535 | 0.00041233 | 0.0012497 | 0.00070599 | 0.0017132
>64 (ms) | 0.002916 | 0.0071196 | 0.011094 | 0.0059361 | 0.011619 | 0.0097668 | 0.0064074 | 0.0077594 | 0.010322 | 0.015408
Notes: Our first observation is that DRAM cells’ charge can be partially restored if it is going to be accessed (i.e., reactivated) soon.
To understand the potential of partial restoration for soon-to-be-reactivated cells,
[click]
we show the distribution of access-to-access intervals.
As demonstrated by prior works that 16ms interval is small enough to yield a reasonable decrease in the restoration latency.
[click]
We break down the interval distributions into five categories based on 16 ms subwindows.
[click]
As shown in the figure, 95% of access-to-access intervals are < 16ms, for which DRAM cells can be partially restored.
[click]
[click]
However, at the time, when we want to perform partial restoration, we actually don’t when the row will be reactivated.
Therefore, although there is great potential there, to exploit such potential, we need someway to predict whether a cell will be reactivated soon (let’s say in the next 16ms)

## Slide 8: Predicting If a Cell Is Reactivated Soon (in 16ms)
Chart: Interval Pair Distribution
| mix1 | mix2 | mix3 | mix4 | mix5 | mix6 | mix7 | mix8 | mix9 | mix10
(Small, Small) | 0.99236 | 0.97216 | 0.94584 | 0.96806 | 0.93599 | 0.93315 | 0.9737 | 0.9764 | 0.95687 | 0.9877
(Small, Large) | 0.0037642 | 0.013852 | 0.027037 | 0.015734 | 0.031699 | 0.032954 | 0.012871 | 0.011769 | 0.021334 | 0.0060402
(Large, Small) | 0.0037786 | 0.013879 | 0.027039 | 0.015745 | 0.031708 | 0.032981 | 0.012887 | 0.011781 | 0.021329 | 0.0060687
(Large, Large) | 9.6714e-05 | 0.00010499 | 7.9853e-05 | 0.00046393 | 0.00060465 | 0.00091233 | 0.00054498 | 4.9665e-05 | 0.00046658 | 0.00019556
The next access-to-access interval of a cell can be accurately predicted by the last access-to-access interval
Prediction:
If the last interval is small, the next interval is small
98% accuracy for 8-core workloads
Notes: To answer the above question, we find that the next access-to-access interval of a cell can be accurately predicted by the last access-to-access interval.
To show this, we study the relationship between last and next access-to-access interval pairs of the same row.
[click]
This figure shows the distribution of last and next access-to-access interval pairs, we define the interval as small if it is less then 16ms, otherwise we define it as large. We group interval pairs into four categories accordingly, small small, small large, large small, and large large.
[click]
As shown in the figure，for 98% of the pairs, if the last access-to-access interval is small, the next access-to-access interval would also be small.
This provides an accurate way for us to predict whether to apply partial restoration.
[click]

## Slide 9: Balancing Activation/Restoration Latency Reductions
We can also reduce the activation latency (tRCD) for DRAM cells with high charge levels [Hassan+ HPCA 2016]
If we maximize the benefits of partial restoration, cells no longer have high charge at activation: we can no longer reduce the activation latency
Time
Bitline Voltage
activation done
full tRCD
reduced tRCD
maximum partial restoration
Notes: On top of reducing the restoration latency, there are other mechanisms that can reduce the activation latency for DRAM cells, as long as it has high charge level
So for example, if you look at this graph here,
[click]
which timeline the accesses with the bitline voltage changes when we activate a cell.
Normally, we have to wait for the full activation latency tRCD,
[click]
But for a fully charged cell, it turns out that we can reduce tRCD significantly.
Unfortunately,
[click]
if we try to maximized the benefits of partial restoration,
[click]
we find that we cann’t reduce tRCD anymore, because it takes almost the complete time for the activation to finish
[click]
So we find that there is a problem: if we maximize the benefits of partial restoration, the cells no longer have high charge when they are activated, and this means we cann’t reduce the activation latency at all.

## Slide 10: Minimizing the Total DRAM Access Latency
We need to trade off the latency reductions of both reduced activation latency and partial restoration
Time
Bitline Voltage
activation done
maximum partial restoration
near-max partial restoration
full tRCD
mostly reduced tRCD
We need to find an optimal balance: reduce most of the activation and restoration latencies
(details in the paper)
Notes: But, we can actually try to trade-off the benefits of both,
So, instead, if we look at a cell,
[click]
Where we get most but not all of the benefits from partial restoration
[click]
We can still get the most of the activation latency reductions at the same time.
[click]
We find that we can trade-off activation and restoration latency reductions in a way that maximized the reduction in total access time.

## Slide 11: Summary of Key Observations
We can apply partial restoration on soon-to-be-reactivated DRAM cells
We can predict with very high accuracy if a cell will be reactivated soon
We can minimize the DRAM access latency by trading off reduced activation latencies and partial restoration
Notes: Let’s summarize our observations:
First, we find that the potential of partial restoration can be significantly improved when applied on soon-to-be-reactivated DRAM cells
[click]
Second, we can accurately predict whether the next access-to-access interval will be smaller than 16ms based on last access-to-access interval
[click]
Third, Although aggressive partial restoration works against activation reduction of highly charged cells,
there exists trade-off between restoration and activation latency reductions. By carefully performing partial restorations, we can maximize the overall benefit

## Slide 12: Background: Accessing Data in DRAM Key Observations on Partial Restoration Charge-Level-Aware Look-Ahead Partial Restoration Evaluation Conclusion
Outline
Notes: Based on the observations, we propose the Charge-level-aware look-ahead partial restoration, we call it CAL.

## Slide 13: Overview of CAL
KEY IDEAS
1. Track and use a DRAM row’s last access-to-access interval to predict whether the row will be reactivated again soon
2. Reduce both the restoration and activation latencies, based on the prediction and next refresh
CAL needs to track
  Last access-to-access interval of each row
  Whether the row was partially restored
We add a timer table to the memory controller
Notes: The key idea of CAL includes two components:
[click]
First, CAL tracks and uses the last access-to-access interval of a row to predict whether the row will be reactivated again soon
[click]
Second, based on the prediction and next scheduled refresh, CAL decides by how much the restoration latency should be reduced to achieve the benefits of both activation and restoration latency reductions.
[click]
To achieve this, cal needs to track the last access-to-access interval of each accessed row, and record whether the row was partially restored.
We employ a timer table to do this

## Slide 14: Tracking Access-to-Access Intervals
When a row is accessed initially
  Insert an entry in the timer table
  Initialize the entry’s timer to 15ms
Timer counts down every 1ms
When a row is accessed again, check the timer in the table
  < 1ms since last access: apply both partial restoration and reduced activation
  1ms –15ms since last access: use only partial restoration
If timer reaches 0, or if entry is evicted
  Fully restore the row if it was partially restored before
Tag
Timer Table
Insert
[PRE]
Counts down
Every 1ms
Initialize
[PRE]
Timer
V
PR
Notes: Here are the major operations when tracking access-to-access intervals
when a DRAM row is accessed initially
[click]
An entry is inserted in the table
[click]
The corresponding timer is initialized
[click]
The timer in each entry counts down every 1 ms
[click]
When a row is accessed again, depending on the timer value
[click]
If less than 1ms has elapsed, CAL employs both partial restoration and reduced activation
[click]
If between 1 and 15 ms has elapsed, CAL employs only partial restoration, because the charge level is not high enough to reduce activation latency
[click]
If the timer reaches 0, or if the entry is evicted,
[click]
we need to fully restore the row if it was partially restored before.

## Slide 15: Background: Accessing Data in DRAM Key Observations on Partial Restoration Charge-Level-Aware Look-Ahead Partial Restoration Evaluation Conclusion
Outline
Notes: Now, let’s discuss our evaluation

## Slide 16: Evaluation Methodology
Simulation Platform
  Ramulator: open-source DRAM simulator [Kim+, CAL’15] https://github.com/CMU-SAFARI/ramulator
  Energy model: includes CPU, caches, off-chip links, and DRAM
CAL Parameters
  8-way cache-like set-associative timer table
  256 entries, LRU replacement policy
  Area overhead: 0.11% of a 16MB last-level cache
20 single-core workloads
  SPEC CPU2006, TPC, BioBench, Memory Scheduling Championship
  Categorized into memory intensive and memory non-intensive
20 eight-core multiprogrammed workloads
  Vary the memory intensiveness from 25% to 100% of applications
Baseline: DDR4 DRAM
Notes: We use DRAM simulator Ramulator for performance evaluation, and build an energy model with CPU, caches, off-chip link, and DRAM.
[click]
We set the timer table as 8-way cache-like set associative structure with 256 enties. We use LRU replacement policy
The area overhead is about 0.11% of a 16MB last-level cache
[click]
We employ 20 single-core workloads from multiple benchmark suits and categorize them into memory intensive and non-intensive groups.
We also form 20 8-core workloads by randomly choosing from single-core workloads, and vary the memory intensiveness from 25% to 100%
[click]
We use an aggressive DDR4 baseline

## Slide 17: Comparison Points
Base: Baseline DDR4 configuration
CC: ChargeCache
  Reduces activation latency for highly-charged rows
  [Hassan+, HPCA ’16]
RT: Restore Truncation
  Reduces restoration latency for soon-to-be-refreshed rows
  [Zhang+, HPCA ’16]
CCRT: combination of ChargeCache and Restore Truncation
IdealCAL: idealized version of CAL
Notes: Besides CAL and our baseline
[click]
We also evaluate ChargeCache (CC), which reduces the activation latency for highly-charged rows
[click]
Restore Truncation (RT), which reduces restoration latency for soon-to-be-refreshed rows
[click]
The combination of activation and restoration latency reductions
[click]
And idealized CAL, in which all rows are accessed with reduced activation and restoration latencies.

## Slide 18: Performance Improvement Over DDR4 Baseline
Chart: Normalized Performance
| Memory Non-Intensive | Memory Intensive | 25% Memory Intensive | 50% Memory Intensive | 75% Memory Intensive | 100% Memory Intensive
CC | 1.0023 | 1.0684 | 1.0169 | 1.0689 | 1.1156 | 1.1286
RT | 1.0037 | 1.0622 | 1.0156 | 1.0645 | 1.1081 | 1.1223
CCRT | 1.0041 | 1.0846 | 1.0203 | 1.0775 | 1.129 | 1.1423
CAL | 1.01 | 1.1388 | 1.0376 | 1.1304 | 1.2034 | 1.2281
IdealCAL | 1.0175 | 1.1644 | 1.0509 | 1.1753 | 1.2622 | 1.2824
Single-Core
8-Core
CAL significantly reduces the DRAM access latency 7.4% speedup for single-core workloads
14.7% speedup for eight-core workloads
Notes: Here is the performance gain of CAL and other mechanisms.
The x-axis is the type of workloads, and the y-axis is the performance gain normalized to the baseline DDR4 DRAM
We make three observations:
First, by simply combining [click] activation and [click] restoration latency reduction mechanisms, the overall performance [click] is only slightly improved.
[click]
Second CAL significantly outperforms the other mechanisms and achieves and average performance gain of 7.4% for single-core and 14.7% for 8-core workloads
[click]
Third cal approaches the ideal case, coming within 4.5% on average.
[click]
Overall, CAL significantly reduces the DRAM latency and achieves higher performance gain with the increase of memory intensity.

## Slide 19: Energy Savings Over DDR4 Baseline
Chart: Energy Consumption
| Memory Non-Intensive | Memory Intensive | 25% Memory Intensive | 50% Memory Intensive | 75% Memory Intensive | 100% Memory Intensive
Base | 1 | 1 | 1 | 1 | 1 | 1
CC | 0.99814 | 0.9385 | 0.98173 | 0.95764 | 0.92777 | 0.91249
RT | 0.99721 | 0.94263 | 0.9835 | 0.97201 | 0.9334 | 0.9219
CAL | 0.99 | 0.87546 | 0.96216 | 0.88534 | 0.8329 | 0.80697
CAL is effective at reducing energy consumption 10.1% reduction for memory-intensive single-core workloads
11.3% reduction for eight-core workloads
Single-Core
8-Core
Notes: This figure shows the energy reduction of CAL
Here the y-axis shows the energy normalized to the baseline
[click]
On average, CAL reduces system energy by 10.1% for memory intensive single-core and 11.3% for 8-core workloads
Overall, CAL is effective at reducing energy consumption, due to the reduction of DRAM latency

## Slide 20: Other Results in Our Paper
Explanations for access-to-access interval distribution
Detailed analysis of the trade-off between activation and restoration latency reductions
Handling large access-to-access intervals in the timer table
Sensitivity studies on
  Timer table size
  Restoration level
  Row management and address mapping policies
  DRAM temperature
Notes: We have other results in the paper
Including explanations of access-to-access interval distribution,
[click]
detailed analysis of the trade-off between activation and restoration latency reductions
[click]
And how to handle large access-to-access intervals to maintain data integrity
[click]
We also perform many sensitivity studies on timer table size, Restoration level
Row management / address mapping policy
Temperature effect

## Slide 21: Conclusion
DRAM access latency is the performance bottleneck
Key observations
  There is significant potential to reduce latency if we partially restore DRAM cells that will be reactivated soon
  If we reduce restoration too much, we cannot use mechanisms that reduce the activation latency: need to strike a balance
CAL: Charge-Level-Aware Look-Ahead Partial Restoration
  Track and use a DRAM row’s last access-to-access interval to predict whether the row will be reactivated again soon
  Reduce both the restoration and activation latencies, based on the prediction and next refresh
Significant DRAM access latency reductions at low cost: 14.7% speedup, 11.3% energy reduction 8-core workloads
Notes: To conclude, DRAM latency is the performance bottleneck
[click]
We observe that the potential of partial restoration can be significantly increased when applied on cells that will be accessed again soon
We also find that we can trade-off between restoration and activation latency reductions to achieve the benefits of both
  [click]
  Based on our observations, we propose CAL, whose key idea is
  first, CAL predicts the next access-to-access interval
  And then it Applies partial restoration based on the prediction and trade-off between restoration and activation latency reductions, and achieves the benefits of both.
  On average,
  [click]
  CAL achieves 14.7% performance improvement and
  11.3% of energy reduction for 8-core workloads

## Slide 22: Reducing DRAM Latency via Charge-Level-Aware Look-Ahead Partial Restoration
Yaohua Wang, Arash Tavakkol, Lois Orosa, Saugata Ghose,
Nika Mansouri Ghiasi, Minesh Patel, Jeremie S. Kim,
Hasan Hassan, Mohammad Sadrosadati, Onur Mutlu
October 22, 2018
Notes: Thank you very much

## Slide 23: Backup Slides

## Slide 24: Partial Restoration
Partial restoration parameters
  Conservatively chosen timing parameters
  Charge level aware rather than aggressive partial restoration
Possible combination with DRAM profiling mechanisms to apply partial restoration only on strong cells, that can hold their charge level for a longer time
  Studies for cell profiling
  [Patel+, ISCA2017]
Notes: Only apply partial restoration on DRAM rows that will be accessed again in 16ms
  Equivalent to reconsider restoration under the refresh interval of 16ms
  Opportunities exist to reduce restoration latency

## Slide 25: 15ms VS 16ms
Our analysis for access-to-access interval is based on the 16ms sub-window (Section 3 in the paper)
  Demonstrated by prior work,16ms is small enough to yield reasonable restoration latency reductions
  Smaller interval does not add much
Our timer table design employs a 4-bit timer, which can count down from 15
  This provides us at least 1ms redundancy for us to issue ACT/PRE (i.e. fully restore), when the timer reaches 0.
  Redundancy is necessary because DRAM commands have to obey timing constraints, there maybe some scheduled commands/refresh waiting to finish their operations.
  1ms seconds is large enough to guarantee that we can save the partially restored charge level

## Slide 26: Per-core Timer Table Design
The timer table can be implemented as either a single shared table or as per-core tables.
In our evaluation, we assume that each core has a dedicated timer table.
We choose per-core timer tables to avoid the need to tune the
optimal size of a shared table based on the core count, and to simplify table organization.
Notes: Again, the time table does not have to be per-core, it can be shared by multi-cores

## Slide 27: Memory Intensity and Access Interval
According to our analysis, memory intensity has little effect on our interval distribution
Mix1-5: 25% memory intensive; Mix6-10: 50% memory intensive; Mix11-15, 75% memory intensive; 100% memory intensive

## Slide 28: What If Applications with Large Access Intervals
Our analysis of access intervals in Section 3 comes from a wide variety of benchmarks from multiple benchmark suits
  SPEC CPU2006, TPC, BioBench, Memory Scheduling Championship
The access locality contribute to our accuracy of interval prediction
16ms access interval is large enough to filter out the diversities among benchmarks, leading to a high prediction accuracy
  With decrease interval (e.g., 8ms), the prediction accuracy would decrease by roughly 10%
While applications with mostly >16ms access-to-access interval may exist, they tend to be memory-none intensive, memory latency is not as critical

## Slide 29: The Uniform Interval Distributions
Refresh happens at fixed time intervals, independent of the memory access pattern.
Due to a combination of the access locality and the high number of row conflicts
16ms interval helps to filter out the diversities of distributions
Notes: Refresh happens at fixed time intervals, independent of the memory access pattern.
As a result, when we divide the refresh interval into four 16 ms sub-windows, the number of memory accesses that fall into each sub-window tends to be similar
Due to a combination of the access locality of applications, and the high number of row conflict that occur due to bank conflicts, As a result, a row that is to be accessed again is likely to be first closed due to a bank conflict and then reactivated for the next access
we find significant diversity in the access-to-access interval distribution if we study smaller sub-windows (e.g., 8ms)

## Slide 30: Handling Large Access-to-access intervals
Two cases to save data by ACT and PRE command pairs
  Miss prediction: when a row timer reaches zero
  Fail to track the partially restored row: when an entry is evicted
  An (ACT, PRE) command pair issued immediately
1ms redundancy is provided to guarantee timing requirement
Less than 0.1% of performance overhead introduced by the (ACT, PRE) command pairs

## Slide 31: Trade-off between tRCD and tRAS reduction
Heuristic of the trade-off
  Vx is the voltage level a DRAM cell is partially restored to. According to our conservative estimation it should be between 0.75Vdd to 0.975Vdd
  We choose 0.85Vdd as the optimal Vx that maximizes PRBenefit

## Slide 32: 3. Area and Power Overhead
Per-core 256-entry timer table
7.7KB with 0.034mm2 area overhead, 0.11% of 16MB LLC
0.202mW power consumption, 0.08% of LLC
New commands with reduced activation and restoration latency
  Reserved undefined encoding
  No additional command bus bits are needed
Notes: Fix bank number alignment

## Slide 33: Timer Table Size
A larger table capacity provides higher performance
The improvement diminish at larger table capacities

## Slide 34: Different Restoration Levels
The restoration level plays an important role in balancing between restoration and activation latency reduction.

## Slide 35: Different Refresh Interval
CAL is still effective at reduced refresh intervals
CAL can be extended to support partial refresh
Notes: We have evaluated the temperature effect in a way with multiple refresh rate. First of all, our propose works fine as long as the 64ms refresh interval works fine. For higher temperature, is is a reasonable choice to increase the refresh rate.
We have evaluated the effect of higher refresh rate.
Overall, CAL is robust for higher refresh rates.
For smaller refresh intervals, we linearly scale the maximum access-to-access interval for which
CAL applies partial restoration, to account for the increased rate of charge decay at higher temperatures. For example, for
a 32 ms refresh interval, partial restoration is applied only when the access-to-access interval is less than 8 ms.

## Slide 36: Activation and Restoration Latency Reduction Trade-off
There exists trade-off between activation and restoration latency reductions
Proper partial restoration level
  Achieve significantly reduced restoration latency
  A smaller reduction of activation latency
  Achieving the benefits of both
A simple and effective trade-off heuristic to approximate the maximum benefit from the trade-off (see paper)
Notes: Fortunately, we find that There exists trade-off between activation and restoration latency reductions
[click]
We have demonstrate that with properly chosen partial restoration level, we can Achieve significantly reduced restoration latency
At the cost of a smaller reduction of activation latency.
And achieves the benefits of both activation and restoration latency reductions.
[click]
In our paper, we use a simple heuristic for such trade-off

## Slide 37: Key Idea & Structure of CAL
1. Uses the last access-to-access interval of a row to predict whether the row will be reactivated again soon
2. Reduces both restoration and activation latencies, based on the prediction and next refresh
Tag
Timer Table
Timer
V
PR
  Tag: stores the DRAM row address
  Timer: records the time elapsed since last precharge
  Partial Restored bit (PR): set to 1 when a row is partially restored
  Valid bit (V)
Notes: The key idea of CAL includes two components:
[click]
First, CAL uses the last access-to-access interval of a row to predict whether the row will be reactivated again soon
[click]
Second, based on the prediction and next scheduled refresh, CAL decides by how much the restoration latency should be reduced to achieve the benefits of both activation and restoration latency reductions.
[click]
The key structure of CAL is a timer table built in the memory controller.
Each entry of the table contains a Tag of an accessed DRAM row, a timer, a partial restored bit and a valid bit.

## Slide 38: Exploiting Charge Levels to Reduce Latency
Prior works exploit the charge level of a DRAM cell to reduce the restoration and activation latencies
  High charge level can reduce activation latency
    Cells accessed in the last 1ms
Notes: [click]
Prior works can reduce DRAM latency by exploiting the charge level of a DRAM cell
[click]
One line of works cut down the restoration time, by taking advantage of the fact that refreshes are regularly scheduled.
[click]
As a result, they apply partial restoration to soon-to-be-refreshed rows, reducing the restoration latency.
[click]
Another line of works observe that high charge level can reduce activation latency.
[click]
DRAM cells accessed in the last 1ms tend to have high charge level as very little charge leackage has occurred since last restoration.
[click]
Thus that they can be accessed with reduced tRCD and tRAS

## Slide 39: Exploiting Charge Levels to Reduce Latency
Prior works exploit the charge level of a DRAM cell to reduce the restoration and activation latencies
  DRAM cells’ charge level can be partially restored to reduce Restoration latency
    Partially restore the charge level of soon-to-be refreshed cells
  High charge level can reduce activation latency
    Cells accessed in the last 1ms
Notes: [click]
Prior works can reduce DRAM latency by exploiting the charge level of a DRAM cell
[click]
One line of works cut down the restoration time, by taking advantage of the fact that refreshes are regularly scheduled.
[click]
As a result, they apply partial restoration to soon-to-be-refreshed rows, reducing the restoration latency.
[click]
Another line of works observe that high charge level can reduce activation latency.
[click]
DRAM cells accessed in the last 1ms tend to have high charge level as very little charge leackage has occurred since last restoration.
[click]
Thus that they can be accessed with reduced tRCD and tRAS